## Slide 1: Geospatial Data Models, Formats and Depositories
Instructor: Dr. Eugene Levin, CP

## Slide 2: Class plan (Learning Outcomes)
LO1: What is mapping and why mapping is needed?
LO2: What is different with spatial data compare to data you learned before?
LO3:What questions we can answer by means of GIS?
LO4:What is GIS Technology?
LO5: What Data Models are deployed by GIS?
LO6: Hands-on experience with installation and operations with open-source free QGIS

## Slide 3: How new is mapping?/1000 B.C. map
Ancient Map of the Earth from Babylonia (1000 B.C.)

## Slide 4: Washington’s Farm
In 1766, George Washington made this sketch of his farm…
Notes: 4

## Slide 5: Data Collection for Mapping: Geospatial Engineering from 3600BC till now

## Slide 6: Cartography (was deployed before computers were invented)
Cartography is the art and science of expressing the known physical features of the earth graphically by maps and charts.
Notes: 6

## Slide 7: Reference & Topo Map

## Slide 8: Simple Dot Map http://www.cybergeography.org/atlas/

## Slide 9: Picture Symbols/Icon Map http://tabi.joy.ne.jp/h-tokachigawa/icon/map.gif

## Slide 10: Multivariate Symbol: Chernoff Faces Source: Eugene Turner, Dan Dorling

## Slide 12: GIS – Definitions
A system of computer software, hardware and data, and personnel to help manipulate, analyze and present information that is tied to a spatial location
Introduction to GIS
Source: http://www.gis.com (ESRI)

## Slide 15: The Need for Spatial Information
Data
Information
Knowledge
Understanding

## Slide 16: How spatial data are different?
3D/4D/5D world should be displayed in 2D –mapping projections;
Topology is important characteristics of spatial data.

## Slide 17: Latitude-Longitude
Notes: Latitude is the angle made at the center of the Earth between a place on the globe and a place directly south of it on the equator. It tells you how far north or south you are of the equator.
Longitude is the angle at the center of the Earth between a place on the globe and another place, at the same latitude, directly north of an agreed-upon spot on the equator. It tells you how far east or west you are of the agreed-upon spot.

## Slide 18: Distortion.
Fitting sphere to plane causes stretching or shrinking of features

## Slide 19: Map Projections
Projecting Earth’s surface always involves distortion:
  shape
  area
  distance
  direction
Notes: A globe is the only representation of earth that can truly realistically represent all of these properties. A map projection by nature will distort one or a combination of these properties.

## Slide 20: Map Projections

## Slide 21: Map Projections
Mathematical conversion of the 3-D nature of the earth’s surface onto a flat 2-dimensional plane (screen or map)
(l, j) (x, y)

## Slide 22: UTM

## Slide 23: GIS is deploying datums

## Slide 24
What is circumference of the earth value ?
Who measured it first?
How?

## Slide 25: Datums
Reference frame for locating points on Earth’s surface
  A set of parameters defining a coordinate system on earth’s surface
Defines origin & orientation of latitude/longitude lines
Defines the position of the spheroid relative to Earth’s center.
Notes: A way to conceptualize a datum is that they form the basis for how measurements are organized on the earth’s surface. Datums use the spheroid values as their basis for what they “know” about how the earth is shaped. Datums define the position of a spheroid in terms of the earth’s center.

## Slide 26: Common U S Datums
North American Datum 1927
North American Datum 1983
WGS-84 – used for your labs
GIS systens allows transformation between two coordinate systems that are based on different horizontal geodetic datums.
Notes: 26

## Slide 27: Why should we take care of projections consistency in GIS [Data conflation problem]

## Slide 28: 2. Topology
Topology --knowledge about relative spatial positioning
--managing data cognizant of shared geometry
Topography --the form of the land surface, in particular, its elevation

## Slide 29: Vector Data Model Representing Data using the Vector Model: formal application
point (node): 0-dimension
  single x,y coordinate pair
  zero area
  tree, oil well, label location
line (arc): 1-dimension
  two (or more) connected x,y coordinates
  road, stream
polygon : 2-dimensions
  four or more ordered and connected x,y coordinates
  first and last x,y pairs are the same
  encloses an area
  census tracts, county, lake
1
2
7
8
.
x=7
Point: 7,2
y=2
Line: 7,2 8,1
Polygon: 7,2 8,1 7,1 7,2
1
2
7
8
1
2
7
8
1
1
2
7
8

## Slide 30
Birch
Cherry
I
II
III
IV
1
4
3
Node/Arc/ Polygon and Attribute Data
Relational Representation: DBMS required!(Geocodes)
Spatial Data
Attribute Data
A35
Smith
Estate
A34
2

## Slide 31
Real World
Vector Representation
Raster Representation
Concept of
Vector and Raster
line
polygon
point

## Slide 32: Digital Elevation Model
a sampled array of elevations (z) that are at regularly spaced intervals in the x and y directions.
two approaches for determining the surface z value of a location between sample points.
  In a lattice, each mesh point represents a value on the surface only at the center of the grid cell. The z-value is approximated by interpolation between adjacent sample points; it does not imply an area of constant value.
  A surface grid considers each sample as a square cell with a constant surface value.
Advantages
Simple conceptual model
Data cheap to obtain
Easy to relate to other raster data
Irregularly spaced set of points can be converted to regular spacing by interpolation
Disadvantages
Does not conform to variability of the terrain
Linear features not well represented

## Slide 33: Triangulated Irregular Network
Advantages
  Can capture significant slope features (ridges, etc)
  Efficient since require few triangles in flat areas
  Easy for certain analyses: slope, aspect, volume
Disadvantages
  Analysis involving comparison with other layers difficult
a set of adjacent, non-overlapping triangles computed from irregularly spaced points, with x, y horizontal coordinates and z vertical elevations.

## Slide 34: Geocoding
For example, a record in the tax assessment file should indicate to which school district it belongs to if the average property values of that school district were to be computed
These geographic labels or identifiers are called geocodes and the process of assigning geocodes is called geocoding
Each address in a city may have as many as 200 geocodes associated with it

## Slide 35: TIGER data model
TIGER (Topologically Integrated Geographic Encoding and Referencing) files
Developed by the U.S. Census Bureau for 1990 census, to remove inconsistencies between dime files and maps, experienced in 1980 census

## Slide 36: Grid Index
Spatial Indexing

## Slide 37: Minimum Bounding Rectangle
Study Area
Spatial Indexing

## Slide 38: Spatial Querying in SQL with spatial extensions (Oracle…)
SELECT * FROM LandParcels
WHERE in_window(location, (x1, y1, x2, y2);
SELECT * FROM LandParcels A, LandParcels B
WHERE adjacent(a.location, b.location) and a.parcel_ID = 1234;
Data Querying

## Slide 39: Query builder in ArcGIS
Supported keywords*
  CURRENT_DATE
  DATE – IN
  ORDER – OR
  NULL – NOT
  LIKE – IS
  DESC – ASC
  AND – SELECT
  FROM – WHERE
Good samples for spatial query in QGIS(tool you will use for your labs) can be found here: https://www.qgistutorials.com/en/docs/3/performing_spatial_queries.html

## Slide 40: GIS Technology

## Slide 41: GIS Data
Census Tracts
Roads
Bus Routes
Shopping Centers
Industrial Sites
From: The Geographer's Craft, Department of Geography, University of Colorado at Boulder
Introduction to GIS

## Slide 42: Summary
• A GIS uses data to describe our world
in two ways:
• With Location Data - Where is it?
• With Attribute Data - What is it?
GIS software maintains a link between layers of location and attribute data
• With this link, we can ask questions about our world… and get useful answers

## Slide 43: GIS data obtaining technologies
Earth Observation Systems
Terrestrial, Aerial, Satellite … Platforms

## Slide 44: What is Big Data?
Examples
2
Internet data (images from the web)
Manufacture sensor data
Copyright of logos belong to the companies.
Earth observation data (nasa.gov)
Healthcare data
www.me.mtu.edu
www.slideshare.net
vision.cloudera.com
dataconomy.com
ibmbigdatahub.com
wikimedia.org

## Slide 45: Geospatial Big Data (SBD)
Geo-referenced big data
Examples:
  GPS trajectories
  Check-in records
  Earth observation imagery
geospatial events, e.g., crimes, accidents
Climate model simulations
Why “geospatial” matters?
  Impact everyday life
  Computational challenges
Fbi.gov
geospatial events: highway serial killing
Nasa.gov
Earth imagery
Microsoft.com
Beijing Taxi GPS trajectories
Nooa.gov
Climate model simulation
Image from the web
Mobile app data

## Slide 46: Geospatial Big Data Analytics Applications
6
Precision agriculture
Location based services
arcgis.com
Disaster response (before and after flood)
Disease outbreak detection
cdc.gov
Image from the web
gps4us.com
innovationtoronto.com
sustainableamerica.org

## Slide 47: GIS implementations
Standalone (ArcGIS, Bentley MicroStation)
Web-Based( multi-tier architectures)
Commercial (ESRI, Bentley,MapInfo);
Free open sourced- QGIS
Formats are interoperable (compatible)

## Slide 48: Next things to do
Work on Lab-assignment
Watch videos on BB
Good Luck!